## Slide 1: MRI-Based Brain Tumor Segmentation
By:
Dmitrii Kornienko Svetlana Lukina
Maksim Elistratov
Ivan Valuev

## Slide 2
Segmentation enables precise volume measurements of lesions, essential for monitoring disease progression or therapy response.
Rapid, reliable identification of pathology boundaries informs surgical navigation, radiotherapy targeting, and real-time intervention strategies
Relevance
Need for precise neuro-pathology delineation
Post-analysis
Supporting adaptive treatment planning
Automated segmentation of brain cancer lesions provides pixel-level accuracy

## Slide 3
Dataset structure
Modalities are different types of MRI scans, each providing unique information about brain tissue. They are passed to the model as input channels:
FLAIR – highlights edema
T1CE – shows contrast-enhancing tumor regions
T1 – provides anatomical context
T2 – captures fluid and lesion spread
Input/Output Shapes:
Input: 4 × H × W (modalities as channels)
Output: 4 × H × W (one-hot encoded segmentation for 4 classes)
Dataset Structure (Per Case): Each patient case includes 4 imaging modalities and 1 segmentation label:
t1.nii – T1-weighted MRI
t1ce.nii – T1 with contrast enhancement
t2.nii – T2-weighted MRI
flair.nii – FLAIR modality
seg.nii – Ground truth segmentation mask

## Slide 4: METRICS
Dice WT: Measures overlap for the entire tumor (labels 1, 2, 4 combined).
Dice TC: Measures overlap for the tumor core (labels 1, 4 combined).
Dice ET: Measures overlap for the enhancing tumor (label 4 only).
(i) Location of the tumor in the brain, (ii) Whole brain tumor (WT), (iii) Edema around the tumor (PE), (iv) Tumor enhancement (ET), and (v) Tumor core (TC)
TP — True Positives, FP — False Positives, FN — False Negatives.
A - predicted mask, B - groundtrue mask,
the number of pixels in the intersection
the total number of pixels in each mask

## Slide 5: 2D UNet
Model: 2D U-Net
Spatial Dimensions: 2D.
Output Channels: 4.
Input Channels: 4 (T1, T1ce, T2,FLAIR)
Output Channels: 4 (Segmentation classes: Background, NCR-NET, ED, ET)
Feature Channels: [64, 128, 256, 512, 1024] (encoder) & [512, 256, 128, 64] (decoder)
Downsampling via MaxPool, upsampling via ConvTranspose2d
Each block uses Conv2d → BatchNorm → ReLU ×2
Data preprocessing:
Middle slice calculation: volume_slices // 2
Range: middle_slice ± (slices_per_volume // 2)
Slices per volume: 16 (slices_per_volume)
Loss Function:
Categorical Dice Loss = CrossEntropy + Dice Loss
One-hot encoded targets used for Dice computation
Training Setup:
Optimizer: Adam, LR = 5e-5
Warmup Scheduler: LinearLR for 5 epochs
Main Scheduler: ReduceLROnPlateau
Evaluation Metrics:
Mean Dice Coefficient across all classes
Per-class Dice scores (NCR-NET, ED, ET)
Combined loss (CE + Dice)

## Slide 6: 2D UNet Segmentation Results

## Slide 7: 3D UNet (common)
Model: 3D U-Net
Spatial Dimensions: 3D.
Input Channels: 4.
Output Channels: 4.
Feature Channels: (64, 128, 256, 512).
Strides: (2, 2, 2).
Residual Blocks: 2.
Dropout Rate: 0.6.
Loss Function:
Categorical Dice Loss = CrossEntropy + Dice Loss
One-hot encoded targets used for Dice computation
Training Setup:
Optimizer: Adam, LR=1e-4
LR Scheduler: ReduceLROnPlateau
Early Stopping: patience=5 epochs
Evaluation metric: Mean Dice Coefficient

## Slide 8: 3D UNet (common)

## Slide 9: 3D UNet (enhanced)
Model: 3D U-Net
Spatial Dimensions: 3D.
Input Channels: 4.
Output Channels: 4.
Feature Channels: (128, 256, 512, 1024).
Strides: (2, 2, 2).
Residual Blocks: 4.
Dropout Rate: 0.9.
Loss Function:
Categorical Dice Loss = CrossEntropy + Dice Loss
One-hot encoded targets used for Dice computation
Training Setup:
Optimizer: Adam, LR=1e-4
LR Scheduler: ReduceLROnPlateau
Early Stopping: patience=10 epochs
Evaluation metric: Mean Dice Coefficient

## Slide 10: 3D UNet (enhanced)

## Slide 11: SwinUNETR
Model: 3D U-Net
Input Resolution: (96, 96, 32).
Input Channels: 4.
Output Channels: 4.
Feature Dimension: 48.
Dropout Rates: 0.0 (standard, attention, path).
Checkpoint Usage: Disabled (False).
Loss Function:
Categorical Dice Loss = CrossEntropy + Dice Loss
One-hot encoded targets used for Dice computation
Training Setup:
Optimizer: Adam, LR=1e-4
LR Scheduler: ReduceLROnPlateau
Early Stopping: patience=10 epochs
Evaluation metric: Mean Dice Coefficient

## Slide 12: SwinUNETR

## Slide 13: SAM / MedSAM / SAM-Med3D
Segment Anything Model (SAM) is a general-purpose image segmentation model that can extract objects from images without additional training.
Architecture: an image encoder, a hint encoder, and a mask decoder.
MedSAM
MedSAM is an adaptation of SAM for medical image segmentation.
The model was trained on a large medical dataset of over 1.5 million image and mask pairs, covering 10 different modalities and over 30 cancer types.
SAM-Med3D
SAM-Med3D extends SAM to 3D medical images.
The model was trained on the large 3D medical dataset SA-Med3D-140K, which includes 22,000 3D images and 143,000 corresponding masks.

## Slide 14: Why we didn't use SAM / MedSAM / SAM-Med3D
Model | Required input | Comment
SAM (2D) | RGB image + bounding box | It is necessary to manually or automatically mark the bbox for each slice
MedSAM (2D) | (H, W, 3) RGB + mask to PNG | Requires 3D modal conversion to 2D RGB, normalization and resizing to 1024x1024, and mask conversion
SAM-Med3D | 3D tomograms format (1, D, H, W) | Requires a single-channel image and a binary mask - not directly suitable for multi-class segmentation
In short: Data preparation requires massive processing and rigorous modification of the structure.
Remind our dataset structure:
4 MRI modalities: flair, t1, t1ce, t2
1 multi-class segmentation mask (0 — background, 1-3 — tumor classes)
Dimensionality: (C=4, D=240, H=240, W=155)

## Slide 15: Thanks for listening!